## Slide 1
Setup: Ensure both your laptop and another device (such as a smartphone or a second laptop) are connected to the exact same Wi-Fi network.
Finding the Target IP: On the phone or target device, check the Wi-Fi settings to note down its assigned local IPv4 address (e.g., 192.168.1.15).
Running the Ping Command:
  Open the Command Prompt (cmd) on your laptop.
  Type ping 192.168.1.15 and press Enter.
Observation: If communication is successful, you will see continuous packet replies showing packet size, response time (latency in milliseconds), and TTL (Time to Live) values with 0% packet loss.
Ping Test Between Laptop and Another Device

## Slide 2
Traceroute to YouTube ([www.youtube.com](https://www.youtube.com))
Running the Command: Open Command Prompt and type:DOS
tracert www.youtube.com
DOS
tracert www.youtube.com
Analysis of Hops: The command traces the path packets take across the internet to reach YouTube's servers.
Typical Observations: It typically takes between 10 to 18 hops depending on your ISP. The first hop is your local router gateway (192.168.1.1), followed by multiple intermediate ISP routing nodes, regional exchange servers, and finally YouTube's edge network servers.

## Slide 3
Pinging a Disconnected Device
Action: Disconnect the target test device (smartphone) completely from the Wi-Fi network.
Retrying the Ping: Run the ping command again from your laptop (ping 192.168.1.15).
Observed Error Messages: Because the device is offline and no longer recognized on the local network, you will receive failure error messages such as:
  “Request timed out.”
  “Destination host unreachable.”

## Slide 4
ARP Table Listing (arp -a)
Running the Command: Open Command Prompt and type arp -a to view the Address Resolution Protocol cache mapping IP addresses to physical MAC addresses.
Sample Device Identification Table:
IP Address | Physical (MAC) Address | Type | Identified Device / Gadget
192.168.1.1 | ac-84-c6-xx-xx-xx | Dynamic | Main Wi-Fi Router / Gateway
192.168.1.15 | 74-da-da-xx-xx-xx | Dynamic | Personal Smartphone (Android)
192.168.1.20 | 28-f0-76-xx-xx-xx | Dynamic | Laptop Computer
192.168.1.25 | b4-e6-2a-xx-xx-xx | Dynamic | Smart TV / Streaming Box

## Slide 5
Network Setup and Testing Report
Network Testing & Connectivity Report
Date: October 26, 2026
Topic: Basic Network Setup, Connectivity Verification, and Diagnostic Testing
Objective: To establish a local network connection, map connected hardware, and test network pathways using ping, tracert, and arp.
1. Network Setup & Configuration
The local network was established by connecting client devices (laptop and mobile phone) to a wireless router operating on a standard private subnet (192.168.1.0/24). Dynamic Host Configuration Protocol (DHCP) automatically assigned unique IPv4 addresses, subnet masks (255.255.255.0), and the default gateway (192.168.1.1) to all participating client nodes.
2. Connectivity Testing (Ping & ARP)
To verify local communication between devices on the same LAN, the ping utility was executed between the laptop and a smartphone.
Successful round-trip times (RTT) averaged between 2ms to 5ms, confirming stable wireless link quality.
Running the arp -a command successfully revealed the hardware MAC addresses corresponding to active local IPs, verifying how the data link layer maps physical interfaces to network layer addresses.

## Slide 6
3. Path Analysis (Traceroute)
To test wide-area network (WAN) routing performance, tracert [www.youtube.com](https://www.youtube.com) was executed.
The trace demonstrated how data packets traverse multiple routers across different autonomous systems.
Initial hops showed rapid transit through local ISP switches, while subsequent hops exhibited higher latency as packets crossed regional fiber backbones to reach content delivery network (CDN) nodes.
4. Troubleshooting & Error Observations
When testing connectivity to a device disconnected from the network, the ping utility returned "Request timed out" errors. This confirmed that network layer reachability depends entirely on active association and proper DHCP/IP state binding.
No major bottlenecks or packet drops were observed during local testing, confirming healthy link integrity.